|  | QUOTATION SCHEDULE B |
| --- | --- |

RFQ Title:	SUPPLY AND DELIVERY OF TWO (2) THREE QUARTER TON
HIGH ROOF DUAL FUEL (CNG & GASOLINE) VANS

RFQ No:	1220-040-2016-031

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email for PDF Files:	purchasing@surrey.ca

1.	If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

2.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

3.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

| F.O.B. Destination, Freight Prepaid | Payment Terms: A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. | Ship Via: |
| --- | --- | --- |
| The Contractor will provide all labour, plant, materials, tools and equipment necessary for the supply and delivery of two (2) 2016 model ¾ ton high roof dual fuel (CNG & Gasoline) cargo vans: |
| Item # | Item Name | Quantity | U/M | Unit Price | Total Amount |
| 1 | ¾ Ton High Roof Dual Fuel (CNG & Gasoline) Van | 2 | Each | $ | $ |
| 2 | Environmental Levy (Battery) | 2 | Each | $ | $ |
| 3 | Tire Stewardship BC (TSBC) Levy | 2 | Each | $ | $ |
| 4 | Options: specify |  |  | $ | $ |
| 5 | Options: specify |  |  | $ | $ |
| Note: The above amounts include, but are not limited to: import duties, brokerage fees, royalties, handling charges, overhead, profit and all other costs included. |  |
| CURRENCY: Canadian | Subtotal: | $ |
|  | GST (5%): | $ |
|  | PST (7%): | $ |
|  | TOTAL: | $ |

4.		Contractor to provide the number of business days for delivery upon the receipt of a Purchase Order:

5.		Contractor to provide year, make, and model:

6.	Contractor to provide the following information:

- Max towing capacity in lbs., including GCWR

- Engine configuration, size, HP, torque specifications

- Number of speeds for the automatic transmission

- Size and number of CNG tanks

7.	Contractor to provide location of the nearest factory authorized warranty repair facility / parts dealership:

8.	State Manufacturer’s Warranty with CNG conversion:

9.	State Body Warranty:

10.	Warranty repairs shall be performed at:

11.	The Contractor is to indicate on each line provided below if they meet or exceed the specifications, Yes or No. If No, any deviations from the stated specifications should be supported by the manufacturer or dealer’s detailed description of each variation with reference made to each item to which the variation will apply. Contractor should attach additional page(s) as required to fully explain any deviations from the stated specifications. If more than one (1) make or model is offered, Contractor is to submit separate specification sheets for each item to be evaluated. Contractor is to indicate if alternate equivalent product certified by manufacturer attached YES    NO .

Contractors should list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications:

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Goods Offered. Contractor should complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour – White. | □ | □ |  |
| 1.2 Vans shall have one sliding door on passengers side for access to the cargo area. | □ | □ |  |
| 1.3 Rear doors and the sides of the van shall have no windows. | □ | □ |  |
| 1.4 Heated external rear vision mirrors. | □ | □ |  |
| Axles, Suspension, Chassis |
| 2.1 The GVWR should be approximately 9,000lbs. | □ | □ |  |
| 2.2 Comes with heavy duty trailer hitch package, c/w receiver, hitch to match the maximum towing capability of the vehicle. Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller. | □ | □ |  |
| 2.3 Wheelbase should be approximately 148”. | □ | □ |  |
| Engine - Transmission |
| 3.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and to comply with all Provincial and Federal engine emission regulations. | □ | □ |  |
| 3.2 Extended life coolant 50/50 mix. The cooling system should be protected to -30o F. | □ | □ |  |
| 3.3 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable. | □ | □ |  |
| 3.4 The vehicles shall default to run on CNG, and only operate on gasoline when the CNG tanks are empty. A strategically placed (hidden) switch to change between the two fuels should be installed. |  |  |  |
| 3.5 Automatic transmission. | □ | □ |  |
| Brakes |
| 4.1 Brakes should be vacuum/hydraulic type with ABS. | □ | □ |  |
| Fuel |
| 5.1 The manufacturers gasoline fuel tank is to remain. | □ | □ |  |
| 5.2 CNG tank(s) are to be rated @ 3600 psi and mounted under the floor of the van. | □ | □ |  |
| 5.3 Fuel gauge for each fuel type is to be provided in easy view for the driver. | □ | □ |  |
| 5.4 CNG filling port should be located in the same area at the gasoline tank filler. | □ | □ |  |
| Wheels, Tires |
| 6.1 Wheels are to be fitted with winter tires (snow flake). | □ | □ |  |
| Interior |
| 7.1 Vehicle interior environment should be fully air-conditioned including a fresh air heater/ventilator/defroster. | □ | □ |  |
| 7.2 Vehicle should have full flow through ventilation for optimal temperature control and operator comfort. | □ | □ |  |
| 7.3 Wipers should have intermittent feature. | □ | □ |  |
| 7.4 Door windows should be power operated. | □ | □ |  |
| 7.5 Vehicle should include dash mounted cigar lighter type power outlet. | □ | □ |  |
| 7.6 Vehicle should include AM/FM/ radio with (2) speakers minimum and antenna. | □ | □ |  |
| 7.7 Rubber Floor Mats should be provided for all seating areas. | □ | □ |  |
| 7.8 Vinyl covered front bucket seats. | □ | □ |  |
| 7.9 Driver and passenger air bags, including side curtain. | □ | □ |  |
| 7.10 Bluetooth connection. | □ | □ |  |
| 7.11 Cruise control. | □ | □ |  |
| Miscellaneous |
| 8.1 Keyless entry with 4 sets of keys. | □ | □ |  |
| 8.2 Back up alarm - Grote part # 73040 97 dBA. | □ | □ |  |
| 8.3 Fire extinguisher 2.5lb dry powder ABC type. | □ | □ |  |
| 8.4 Front and rear mud flaps. | □ | □ |  |
| 8.5 Reverse Camera. | □ | □ |  |

12.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this ________ day of ________________, 201_

| CONTRACTOR I/We have the authority to bind the Contractor. ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |