|  | QUOTATION SCHEDULE B |
| --- | --- |

RFQ Title:	6 (MORE or LESS) DUAL FUEL 16,500lb and 19,000lb TRUCKS

RFQ No:	1220-040-2016-078

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

All costs to meet the preferred specifications should be included in the following delivered prices.

1.A.	ONE TON (16,500 LBS GVW) REGULAR CAB, 4x2, CAB & CHASSIS CONFIGURATION

Year, Make & Model:  __________________________________________________________

All costs to meet the minimum specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | ONE TON (16,500 LBS GVW) REGULAR CAB, CAB & CHASSIS CONFIGURATION 4x2 – MR16-125 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | ONE TON (16,500 LBS GVW) REGULAR CAB, CAB & CHASSIS CONFIGURATION 4x2 – MR16-126 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification will cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Minimum Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 Cab & Chassis, 84 inch CA, wheel base approx. 165 inch | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Install window vent visors on both front doors | □ | □ |  |
| Engine |
| 2.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and shall comply with all Provincial and Federal engine emission regulations | □ | □ |  |
| 2.2 State engine configuration, size | □ | □ |  |
| 2.3 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.4 Cooling system to -30F | □ | □ |  |
| 2.5 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be of a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 CNG fuel tank(s) to be mounted in tool box as provided by body supplier in a manner to maximize box space | □ | □ |  |
| 4.5 CNG filling port shall be located between the cab and the tool box | □ | □ |  |
| Wheels, Tires |
| 5.1 All Terrain tires | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 Seat covers shall be installed – fabric type Wrangler – Fia Saddle Blanket type | □ | □ |  |
| 6.3 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.4 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.5 Air conditioning | □ | □ |  |
| 6.6 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 3 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 State GVW in lbs | □ | □ |  |
| 7.4 State max towing capacity in lbs | □ | □ |  |
| 7.5 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.6 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.7 WCB Level 1 Basic First Aid Kit | □ | □ |  |
| 7.8 Splash guards front and rear | □ | □ |  |
| 7.9 Running boards shall be supplied and fitted | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |
| 10. Dumpbox Package |
| 10.1 Dumpbox package(s) as per Work Truck West MR16-125 and MR16-126 Please provide pricing for both dumpbox packages | □ | □ |  |

- END OF PAGE –

1.B. ONE TON (16,500 lb GVW) REGULAR CAB 4X4, CAB & CHASSIS CONFIGURATION

Year, Make & Model:  __________________________________________________________

All costs to meet the minimum specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | ONE TON (16,500 LBS GVW) REGULAR CAB 4X4, CAB & CHASSIS CONFIGURATION – MR16-125 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | ONE TON (16,500 LBS GVW) REGULAR CAB 4X4, CAB & CHASSIS CONFIGURATION – MR16-126 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification will cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Minimum Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 Cab & Chassis, 84 inch CA, wheel base approx. 165 inch | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Install window vent visors on both front doors |  |  |  |
| Engine |
| 2.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and shall comply with all Provincial and Federal engine emission regulations | □ | □ |  |
| 2.2 State engine configuration, size | □ | □ |  |
| 2.3 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.4 Cooling system to -30F | □ | □ |  |
| 2.5 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| 3.4 Front axle shall have freewheeling hubs | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be of a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable. State tank size | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 CNG fuel tank(s) to be mounted in tool box as provided by body supplier in a manner to maximize box space | □ | □ |  |
| 4.5 CNG filling port shall be located between the cab and the tool box | □ | □ |  |
| Wheels, Tires |
| 5.1 All Terrain tires | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 Seat covers shall be installed – fabric type Wrangler – Fia Saddle Blanket type |  |  |  |
| 6.3 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.4 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.5 Air conditioning | □ | □ |  |
| 6.6 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 3 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 State GVW in lbs | □ | □ |  |
| 7.4 State max towing capacity in lbs | □ | □ |  |
| 7.5 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.6 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.7 WCB Level 1 Basic First Aid Kit |  |  |  |
| 7.8 Splash guards front and mudflaps rear | □ | □ |  |
| 7.9 Running boards shall be supplied and fitted | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature.. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |
| 10. Dumpbox Package |
| 10.1 Dumpbox package(s) as per Work Truck West MR16-125 and MR16-126 Please provide pricing for both dumpbox packages | □ | □ |  |

- END OF PAGE –

1.C. 19,500 LBS GVW (MINIMUM) REGULAR CAB, CAB & CHASSIS CONFIGURATION 4x2

Year, Make & Model:  __________________________________________________________

All costs to meet the minimum specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | 19,500 LBS GVW (MINIMUM) REGULAR CAB, CAB & CHASSIS CONFIGURATION 4x2 – MR16-125 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | 19,500 LBS GVW (MINIMUM) REGULAR CAB, CAB & CHASSIS CONFIGURATION 4x2 – MR16-126 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification will cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Minimum Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 Cab & Chassis, 84 inch CA, wheel base approx. 165 inch | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Install window vent visors on both front doors |  |  |  |
| Engine |
| 2.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and shall comply with all Provincial and Federal engine emission regulations | □ | □ |  |
| 2.2 State engine configuration, size | □ | □ |  |
| 2.3 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.4 Cooling system to -30F | □ | □ |  |
| 2.5 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential |  |  |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable. State tank size | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 CNG fuel tank(s) to be mounted in tool box as provided by body supplier in a manner to maximize box space | □ | □ |  |
| 4.5 CNG filling port shall be located between the cab and the tool box | □ | □ |  |
| Wheels, Tires |
| 5.1 Michelin winter tires (snow flake) | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 Seat covers shall be installed – fabric type Wrangler – Fia Saddle Blanket type |  |  |  |
| 6.2 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.3 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.4 Air conditioning | □ | □ |  |
| 6.5 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 4 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 State GVW in lbs | □ | □ |  |
| 7.4 State max towing capacity in lbs | □ | □ |  |
| 7.5 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.6 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.7 WCB Level 1 Basic First Aid Kit |  |  |  |
| 7.8 Splash guards front and mudflaps rear | □ | □ |  |
| 7.9 Running boards shall be supplied and fitted | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature.. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |
| 10. Dumpbox Package |
| 10.1 Dumpbox package(s) as per Work Truck West MR16-125 and MR16-126 Please provide pricing for both dumpbox packages | □ | □ |  |

- END OF PAGE –

1.D. QUOTATION 9 – 19,500 LBS GVW (MINIMUM) REGULAR CAB 4X4, CAB & CHASSIS CONFIGURATION

Year, Make & Model:  __________________________________________________________

All costs to meet the minimum specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | 19,500 LBS GVW (MINIMUM) REGULAR CAB 4X4, CAB & CHASSIS CONFIGURATION – MR16-125 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | 19,500 LBS GVW (MINIMUM) REGULAR CAB 4X4, CAB & CHASSIS CONFIGURATION – MR16-126 |
| VEHICLE QUANTITY | 1 | 3 | 5 | 5+ (PER VEHICLE) |
| PRICE | $________ | $________ | $________ | $________ |
| ENVIRONMENTAL LEVY [BATTERY] | $________ | $________ | $________ | $________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $________ | $________ | $________ | $________ |
| OTHER: |  |  |  |  |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| ____________________________ | $________ | $_______ | $________ | $________ |
| SUBTOTAL | $________ | $________ | $________ | $________ |
| GST 5% | $________ | $________ | $________ | $________ |
| PST 7% | $________ | $________ | $________ | $________ |
| TOTAL QUOTED PRICE: | $________ | $________ | $________ | $________ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification will cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Minimum Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 Cab & Chassis, 84 inch CA, wheel base approx. 165 inch | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Install window vent visors on both front doors |  |  |  |
| Engine |
| 2.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and shall comply with all Provincial and Federal engine emission regulations | □ | □ |  |
| 2.2 State engine configuration, size | □ | □ |  |
| 2.3 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.4 Cooling system to -30F | □ | □ |  |
| 2.5 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| 3.4 Front axle shall have freewheeling hubs | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be of a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable. State tank size | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 CNG fuel tank(s) to be mounted in tool box as provided by body supplier in a manner to maximize box space | □ | □ |  |
| 4.5 CNG filling port shall be located between the cab and the tool box | □ | □ |  |
| Wheels, Tires |
| 5.1 All Terrain tires | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 Seat covers shall be installed – fabric type Wrangler – Fia Saddle Blanket type |  |  |  |
| 6.2 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.3 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.4 Air conditioning | □ | □ |  |
| 6.5 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 4 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 State GVW in lbs | □ | □ |  |
| 7.4 State max towing capacity in lbs | □ | □ |  |
| 7.5 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.6 WCB Level 1 Basic First Aid Kit |  |  |  |
| 7.7 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.8 Splash guards front and mudflaps rear |  |  |  |
| 7.9 Running boards shall be supplied and fitted |  |  |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature.. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |
| 10. Dumpbox Package |
| 10.1 Dumpbox package(s) as per Work Truck West MR16-125 and MR16-126 Please provide pricing for both dumpbox packages | □ | □ |  |

Payment Terms:

A cash discount of ________ % will be allowed if the invoice is paid within _______ days, or the ____ day of the month following, or net 30 days, on a best effort basis.

The completed unit shall be delivered within _______ days after receipt of purchase order.

Complete Vehicle:  State Warranty (no less than one (1) year)

Extended Warranty Options:  __________________________________________________________________________

Warranty repairs shall be performed at

2.		If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

3.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |