|  | SCHEDULE B – QUOTATION |
| --- | --- |

RFQ Title:	SUPPLY AND DELIVERY OF ONE (1) OR MORE 14,500 LBS GVW (MINIMUM)

DUAL FUEL (CNG & GASOLINE) CAB OVER ENGINE CONFIGURATION TRUCK WITH TIPPING DECK SPECIALIST BODY FOR GARBAGE COLLECTION

RFQ No:	1220-040-2018-008

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications should be included in the following delivered prices.

| UNIT PRICE: | $________________ X 1 or more | $______________ |
| --- | --- | --- |
| ENVIRONMENTAL LEVIES (BATTERY): | $________________ X 1 or more | $______________ |
| TIRE STEWARDSHIP B.C. (TSBC): AIR CONDITIONING: OTHER: | $________________ X 1 or more $________________ X 1 or more | $______________ $______________ |
| WORK TRUCK WEST QUOTE: __________________________ | $________________ X 1 or more | $______________ |
| SUBTOTAL: |  | $______________ |
| GST 5% on $ ___________: | HST | $______________ |
| PST 7% on $____________: | HST | $______________ |
| TOTAL QUOTED PRICE: |  | $______________ |

Payment Terms:
A cash discount of ________ % will be allowed if the invoices is paid within _______ days, or the ____ day of the month following, or net 30 days, on a best effort basis.

Delivery of Goods:

The completed unit shall be delivered within _______ days after receipt of purchase order.

Complete Vehicle:  State Warranty (no less than one (1) year)

Extended Warranty Options:  __________________________________________________________________________

Warranty repairs shall be performed at

2.		If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

3.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

-END OF PAGE-

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

_________________________________________ (Print Name and Position of Authorized Signatory)

SCHEDULE B-1 – PREFERRED SPECIFICATIONS

SUPPLY AND DELIVERY OF ONE (1) OR MORE 14,500 LBS GVW (MINIMUM) DUAL FUEL (CNG & GASOLINE) CAB OVER ENGINE CONFIGURATION TRUCK WITH CART DELIVERY BODY

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations shall be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification may cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | Yes (Circle) | No (Circle) | Manufacturers’ Specifications of Equipment Offered. Contractor to indicate compliance or deviation with specifications below. |
| --- | --- | --- | --- |
| Chassis |
| 1.1 Colour - White | Y | N |  |
| 11.2 Chassis should be a cab over engine configuration with 176 inch wheel base approx. & with a 153” CA approx. - to be confirmed with body builder, allowing for a 14’ deck, and 30” toolbox behind cab | Y | N |  |
| 1.3 Heated mirrors | Y | N |  |
| 1.4 State chassis make, model and point of manufacture | Y | N |  |
| Axles, Suspension, Frame |
| 2.1 Chassis shall be a minimum of approx.14,500 lbs. GVW rating | Y | N |  |
| 2.2 State max towing capacity in lbs. | Y | N |  |
| 2.3 Comes with hidden trailer hitch package, c/w receiver, hitch to match the maximum towing capability of the vehicle. Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | Y | N |  |
| 2.4 Rear axle capacity shall be a minimum of 11,000 lbs., with taper leaf springs and shock absorbers | Y | N |  |
| 2.5 Front axle capacity shall be a minimum of 6,600 lbs., with tapper leaf springs and shock absorbers | Y | N |  |
| 2.6 Differential shall be limited slip and comes with synthetic gear oil | Y | N |  |
| 3. Engine - Transmission |
| 3.1 Engine shall be prepared (gaseous prep engine) to run on CNG and gasoline, and shall comply with all Provincial and Federal engine emission regulations | Y | N |  |
| 3.2 State engine configuration, size, HP, torque specifications | Y | N |  |
| 3.3 Full manufactures warranty with CNG conversion must be provided | Y | N |  |
| 3.4 Extended life coolant 50/50 mix. The cooling system shall be protected to -34o F. | Y | N |  |
| 3.5 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | Y | N |  |
| 3.6 The vehicles should default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. | Y | N |  |
| 3.7 Automatic transmission, state number of speeds | Y | N |  |
| 4. Brakes |
| 4.1 Brakes shall be vacuum/hydraulic type with ABS | Y | N |  |
| 4.2 Front brakes shall be disc type, rear brakes shall be drum type | Y | N |  |
| 4.3 Parking brake shall be drum/driveline, internal expanding shoes. | Y | N |  |
| 5. Fuel |
| 5.1The manufacturers gasoline fuel tank shall remain | Y | N |  |
| 5.2 CNG tank shall be of a size of at least 24.5 GGE/93GLE (@3600 PSI) to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable. State tank size | Y | N |  |
| 5.3 Fuel gauge for each fuel type should be provided in easy view for the driver | Y | N |  |
| 5.4 CNG fuel tank to be mounted in the toolbox behind the cab in upper most part of the box. CNG installer to ensure sufficient space is available, discuss with body builder. | Y | N |  |
| 5.5 CNG filling port should be located between the cab and the tool box | Y | N |  |
| 5.6 Valving should be installed in a suitable location to allow for the CNG system to be de-fueled should the need arise | Y | N |  |
| 6. Wheels, Tires |
| 6.1 Rims should be 16 inch diameter | Y | N |  |
| 6.2 Tires should be 10 ply all-season tires in all positions | Y | N |  |
| 7. Cab |
| 7.1 Cab interior environment should be fully air-conditioned including a fresh air heater/ventilator/defroster. | Y | N |  |
| 7.2 Cab should have full flow through ventilation for optimal temperature control and operator comfort. | Y | N |  |
| 7.3 Wipers should have intermittent feature. | Y | N |  |
| 7.4 Door windows should be power operated | Y | N |  |
| 7.5 Cab should include dash mounted cigar lighter type power outlet | Y | N |  |
| 7.6 Cab should include AM/FM/ radio with (2) speakers and antenna, and be Bluetooth capable | Y | N |  |
| 7.7 Rubber Floor Mats should be provided for all seating areas | Y | N |  |
| 7.8 Full vision illuminated instrumentation and warning lights, with tachometer, speedometer, odometer, trip odometer, hour meter, fuel gauge, water temperature gauge, oil pressure gauge, | Y | N |  |
| 8. Miscellaneous |
| 8.1 Keyless entry with 3 sets of keys | Y | N |  |
| 8.2 Trailer Tow Package Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | Y | N |  |
| 8.3 Back up alarm - Grote part # 73040 97 dBA | Y | N |  |
| 8.4 Fire extinguisher 2.5lb dry powder ABC type | Y | N |  |
| 8.5 Front and rear mud flaps | Y | N |  |
| 8.6 LED amber beacon light – Whelen part# R2LPPA | Y | N |  |
| 8.7 Reverse Camera | Y | N |  |
| 8.8 All auxiliary cab switches should be wired from a non-switched source – e.g. direct from battery | Y | N |  |
| 9. Warranty, Service & Training |
| 9.1 Provide details of manufacturer’s warranty | Y | N |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | Y | N |  |
| 9.3 Vendors shall have a full parts and service facility within a reasonable distance from the City Garage. State location and distance | Y | N |  |
| 9.4 A qualified technician should provide complete training to City personnel at the City Garage. Training shall include safety, operation, maintenance and service. | Y | N |  |
| 9.5 The vehicle including the chassis and underside of the body shall be rust proofed with a product that provides long term protection, and does not require continued reapplication of the product. Proponent to provide details of product offered and warranty. | Y | N |  |
| 9.6 The proponent should deliver the vehicles, registered, insured, and plated as per the City’s insurance requirements through the City’s insurance broker. | Y | N |  |
| 10. CART DELIVERY BODY |
| 10.1 A 14’ deck and toolbox as per Work Truck West quote MR17-343. Work Truck contact is Mike Rolleman at 604-590-7269 | Y | N |  |

-END OF PAGE-