|  | QUOTATION SCHEDULE B |
| --- | --- |

RFQ Title:	SUPPLY AND DELIVERY OF ONE (1) OR MORE NEW REDUCED TAIL SWING EXCAVATOR(S) WITH AN OPERATING WEIGHT OF APPROX. 14,000 kg

RFQ No:	1220-040-2016-116

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications should be included in the following delivered prices.

|  | “Without Trade/s” |  |  |
| --- | --- | --- | --- |

| UNIT PRICE: | $________________ X 1 | $______________ |
| --- | --- | --- |
| ENVIRONMENTAL LEVIES: BATTERY: | $________________ X 1 | $______________ |
| AIR CONDITIONING: ANY OTHER LEVIES OR FEES: | $________________ X 1 $________________ X 1 $________________ X 1 | $______________ $______________ $______________ |
|  | SUB-TOTAL: | $______________ |
| GST 5% on $ ___________: . | HST | $______________ |
| PST 7% on $____________: . | HST | $______________ |
| TOTAL QUOTED PRICE: |  | $______________ |

Payment Terms:
A cash discount of ________ % will be allowed if the invoices is paid within _______ days, or the ____ day of the month following, or net 30 days, on a best effort basis.

The completed unit shall be delivered within _______ days after receipt of purchase order.

Complete Vehicle:  State Warranty (no less than one (1) year)

Extended Warranty Options:  __________________________________________________________________________

Warranty repairs shall be performed at

2.		If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

3.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

-END OF PAGE-

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |

RDO Revision May 2016

MAY 21, 2009

U:\LEGALSRV\LEGAL\AGREEMENTS\RFP-Contract-Templates\Documents\Request for Quotations for Goods.doc

saw\lb1-10/14/16 2:40 PM

SCHEDULE B-1 – PREFERRED SPECIFICATIONS

PREFERRED SPECIFICATIONS FOR:  ONE (1) OR MORE NEW REDUCED TAIL SWING EXCAVATOR(S) WITH AN OPERATING WEIGHT OF APPROX. 14,000 kg

Contractor should list complete manufacturer’s details in the right column opposite to the preferred listed requirement.

| Preferred Specifications | Yes (Circle)) | No (Circle)) | Manufacturers’ Specifications of Equipment Offered. Contractor to indicate compliance or deviation with specifications below. |
| --- | --- | --- | --- |
| ENGINE |
| 1.1 Four Cylinder, turbocharged, isolation mounted diesel engine. | Y | N |  |
| 1.2 Engine shall be certified to EPA Tier 4 interim or better. | Y | N |  |
| 1.3 Engine displacement shall be no less than 3 liters. | Y | N |  |
| 1.4 Engine rated net peak power shall be no less than (70 kW) @ 2000 rpm. | Y | N |  |
| 1.5 Engine shall have auto-idle mode to reduce engine speed when hydraulics are not in use to reduce fuel consumption and noise. | Y | N |  |
| 1.6 The engine oil and fuel filters will be remotely mounted for ease of access. | Y | N |  |
| 1.7 Under-hood engine air cleaner shall be dry type, dual element with evacuator valve, restriction sensor and in-cab restriction warning light. | Y | N |  |
| 1.8 Primary fuel filter shall have no more than 30-micron rated primary filter with water separator. | Y | N |  |
| 1.9 Secondary fuel filter shall have no more than a 2-micron rated filter. | Y | N |  |
| 1.10 Engine will be equipped with a water-in-fuel sensor. | Y | N |  |
| 1.11 Engine must have the capability of running on either ultra-low sulfur diesel (ULSD) fuel with 15 ppm of sulfur or less or biodiesel (B20) fuel blended with ULSD that meets ASTM 6751 or EN 14214 standards. | Y | N |  |
| Cooling |
| 2.1 Factory-fill long life coolant rated to –34 F (–37° C), shall be standard – please provide hours/years before change is required. | Y | N |  |
| 2.2 The machine shall be equipped with an oil-to-water engine oil cooler. | Y | N |  |
| 2.3 Unit shall have a coolant recovery tank provided. | Y | N |  |
| 2.4 The radiator and oil cooler will be protected with a trash screen to protect against overheating. | Y | N |  |
| 2.5 The hydraulic circuits will be water cooled. | Y | N |  |
| Power Train |
| 3.1 The excavator shall be two-speed with automatic shift with a high speed of 5.5 km/h. | Y | N |  |
| 3.2 The hydraulic pilot levers shall have short stroke and low effort to reduce fatigue. | Y | N |  |
| 3.3 The Swing brake shall be multiple wet disk, or equivalent, spring applied and hydraulically released. | Y | N |  |
| 3.4 The propel brake shall be spring applied and hydraulically released. | Y | N |  |
| 3.5 Drawbar pull shall be approx. 11,000 kg. | Y | N |  |
| Hydraulic System |
| 4.1 The hydraulic system shall be open center, load sensing. | Y | N |  |
| 4.2 Not less than two main implement pumps shall be provided and pumps shall be variable displacement piston type. Please provide details. | Y | N |  |
| 4.3 Total combined flow from the two implement pumps shall not be less than 58 gal per minute. | Y | N |  |
| 4.4 Factory installed one way/two way; one pump/two pump high pressure hydraulics plus two way medium pressure hydraulics shall be available. Flow settings for up to 10 different hydra-mechanical tools shall be capable of being programmed into the cab monitor to simplify tool selection/changes by the operator. | Y | N |  |
| 4.5 Boom and stick shall have reduced drift valves fitted. | Y | N |  |
| 4.6 An accumulator shall be provided to allow the boom and stick to be lowered to the ground in the case of a dead engine. | Y | N |  |
| 4.7 Factory installed hydraulics to operate a hydraulic “pin grabber” shall be available. | Y | N |  |
| 4.8 A boom and stick regeneration circuit shall be standard to save energy during boom-down and stick-in operation. | Y | N |  |
| 4.9 An auxiliary hydraulic valve shall be standard for use with optional hydraulic circuits. | Y | N |  |
| 4.10 Machine shall be supplied with hydraulic lines to run work tools, and hydraulic “pin grabber”. | Y | N |  |
| 4.11 The machine shall piped and have controls to operate a hydraulic compactor (hoepack) | Y | N |  |
| 4.12 The machine shall be supplied with hydraulically operated “pin grabber” quick coupler. | Y | N |  |
| Electrical |
| 5.1 The electrical system shall be 24 volt and alternator rating no less than 70 amp. | Y | N |  |
| 5.2 Cab shall have a 12 volt, 60 watt, 5 amp cell phone power outlet. | Y | N |  |
| 5.4 Cab will be pre-wired for rotating beacon and 2 way radio-ready. The beacon shall have its own power supply and be switched. | Y | N |  |
| 5.4 Machine shall have HID work lights available on cab, boom and stick for greater visibility. | Y | N |  |
| 5.5 Unit shall be equipped with a Telematics systems that can provide fleet management, logistics and remote diagnostics capabilities. Provide information and ongoing cost of system | Y | N |  |
| 5.6 Machine shall be supplied with a remote “jump start receptacle” | Y | N |  |
| Operators Station |
| 6.1 Machine shall have a Certified ROPS cab meeting ISO 12117-2 specifications. | Y | N |  |
| 6.2 Machine shall have a ROPS Certified cab that allows an Operator Protective Guard (OPG) to be bolted directly to it. | Y | N |  |
| 6.3 Machine shall be capable of accepting a bolt-on FOGS (Falling Object Guard System) system without further cab reinforcement. | Y | N |  |
| 6.4 The cab shall have an openable roof hatch to provide additional emergency escape path and clear visibility to overhead obstacles with a sunshade for operator comfort | Y | N |  |
| 6.5 The operator will be provided with a conveniently located tool to break the window in case of an emergency | Y | N |  |
| 6.6 Cab shall have an automatic climate control system with outlets which provided positive filtered ventilation | Y | N |  |
| 6.7 The A/C filters shall be easy to replace with no special tools required | Y | N |  |
| 6.8 Machine shall have a 3” (75 mm) wide retractable seat belt as standard. | Y | N |  |
| 6.9 Seat shall be adjustable, with suspension, headrest and adjustable lumbar support and adjustable armrests with heating and cooling | Y | N |  |
| 6.10 System shall retain and display active fault codes and incidents related to machine operating outside of the specified parameter | Y | N |  |
| 6.11 Machine shall have a rear view camera available with the ability to view from the cab monitor. | Y | N |  |
| 6.12 Factory installed AM/FM stereo radio shall be standard. | Y | N |  |
| 6.13 The horn and travel alarm shall be operable while the machine is moving forward or in reverse | Y | N |  |
| Boom, Stick, Attachments |
| 7.1 Boom length shall be approx. 4.65m | Y | N |  |
| 7.2 Stick length shall be approx. 3.0m and capable of adding a thumb to it should it be required in the future. | Y | N |  |
| 7.3 An Optional Heavy Counterweight shall be supplied. Please state weight and cost | Y | N |  |
| 7.4 Machine shall have a Front Blade with cutting edge and with a hydraulic float capability to perform leveling operations. | Y | N |  |
| 7.5 Front Blade width shall match track width of machine | Y | N |  |
| 7.6 The machine shall be supplied with 24”, and 32” digging bucket, with smooth plate attached to bucket teeth for cleaning the bottom of trenches, and 54” clean up bucket, all with pins for a “pin grabber” quick hitch. | Y | N |  |
| 7.7 Certified lifting eyes shall be welded to the quick hitch, and all buckets. The eye shall have approx. 25 mm hole through the plate to accommodate a shackle. | Y | N |  |
| 7.8 In addition to the lifting eye, a 3/8” “grab hook” shall be welded to the upper side of the lifting eye on quick hitch and all buckets. | Y | N |  |
| 7.9 A hydraulically operated “pin grabber” shall be supplied and installed – preference given to factory supplied unit | Y | N |  |
| 7.10 A Groeneveld auto grease unit shall be supplied and installed |  |  |  |
| Undercarriage |
| 8.1 Machine shall be supplied with long track frame option | Y | N |  |
| 8.2 Machine shall have as standard equipment, grease lubricated track chains. | Y | N |  |
| 8.3 Track and carrier rollers shall be lubricated for life. | Y | N |  |
| 8.4 Rubber bolt crawler pads shall be bolted to the track shoes to match 20” triple grouser shoes (clamp type are not acceptable). | Y | N |  |
| 8.7 Machine shall have as standard equipment a swivel guard. | Y | N |  |
| 8.8 Machine shall have as standard equipment a towing eye on the base frame. | Y | N |  |
| Warranty |
| 9.1 Proponent to provide details standard warranty coverage. | Y | N |  |
| 9.2 Proponent to provide details and cost of extended machine warranty, including engine and emission systems. | Y | N |  |
| 9.3 Proponent shall provide operator and mechanical orientation of the machine to City staff. | Y | N |  |
| Safety |
| 10.1 Machine shall be supplied with, 1- 2 lb fire extinguisher, 1 – No. 1 first aid kit, Orange LED strobe light (R2LPPA Whelen) wired with its own switch direct to a non-switched power source. | Y | N |  |
| 10.2 Machine shall not be capable of being started with the hydraulic lock lever in the "live" or "run" position. | Y | N |  |
| Regulations |
| Excavator must comply with government regulations and requirements: Federal Government Regulations BC Workers’ Compensation Board Regulations BC Emissions Standards |  |  |  |
| Machine |
| 12.1 Provide operating weight of machine in kg. |  |  |  |
| 12.2 Please provide full specification sheet of proposed machine (Excel format is preferred). | Y | N |  |