|  | QUOTATION SCHEDULE B |
| --- | --- |

RFQ Title:	SUPPLY AND DELIVERY OF ONE (1) SITE OFFICE/LUNCH ROOM TRAILER

RFQ No:	1220-040-2016-077

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

1.	The Contractor offers to supply to the City of Surrey the Goods for the prices plus applicable taxes as follows:

Year, Make & Model:  __________________________________________________________

All costs to meet the minimum specifications shall be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM |  |
| PRICE | $_____________ |
| ENVIRONMENTAL LEVY [BATTERY] | $_____________ |
| TIRE STEWARDSHIP B.C. (TSBC) | $_____________ |
| OTHER: |  |
| ____________________________ | $_____________ |
| ____________________________ | $_____________ |
| ____________________________ | $_____________ |
| SUBTOTAL | $_____________ |
| GST 5% | $_____________ |
| PST 7% | $_____________ |
| TOTAL QUOTED PRICE: | $_____________ |
| CURRENCY: CANADIAN |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified   (

SPECIFICATIONS

The specification herein states the minimum requirements of the City of Surrey. All Quotations must be regular in every respect. Unauthorized conditions, limitations, or provisions shall be cause for rejection. The City of Surrey will consider as "irregular" or "non-responsive" any Quotation not prepared and submitted in accordance with the RFQ document and specification, or any Quotation lacking sufficient technical literature to enable the City to make a reasonable determination of compliance to the specification.

It shall be the Contractor's responsibility to carefully examine each item of the specification. Failure to offer a completed Quotation or failure to respond to each section of the technical specification will cause the Quotation to be rejected without review as "non-responsive". All variances, exceptions and/or deviations shall be fully described in the appropriate section.

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

SITE OFFICE LUNCH ROOM TRAILER

| Minimum Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Contractor shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Outside Cladding and Dimensions |
| 1.1 Colour - White | □ | □ |  |
| 1.2 Approximate overall dimensions: Length 22’6” (od) Width 8’6” (od) Height 7’6” (id) | □ | □ |  |
| 1.3 Walls – shall be SnapLock extrude aluminum panels with nominal 1/8” skin thickness and integral 1”x2” posts @ 12” o.c. Angled cutouts in side walls for wheel well openings | □ | □ |  |
| 1.4 Roof – 10 ga heavy duty “walk on” roof with bows @ 12” o.c., extruded aluminum perimeter roof edge on all sides | □ | □ |  |
| Frame, Running Gear & Bumper |
| 2.1 2”x6” tubular steel longsills with a 7’ A-frame 3” Jr I-beam cross member @ 16” o.c. Bumper: HD Tube bumper with skid plate | □ | □ |  |
| 2.2 Extended A-frame with 2-5/16” adjustable ball coupler 20,000lb capacity (Hitchco #07678-97) plus 3” ID adjustable pintle ring 20,000lb capacity (hitchco #09557-97) with 5 position 3.5” height adjustable channel (Hitchco # B8979) | □ | □ |  |
| 2.3 2 – 24” long 15,000.lb capacity safety chains – 3/8” Grade 70 chain with 3/8” grade 80 latching clevis hooks and 3/8” grade 80 midlinks attached 25” 3/8” x 1.5” steel flat bars each with 12 attachment holes (to suit extenda-hitch) welded below trailer hitch A-frame | □ | □ |  |
| 2.4 The A-frame shall be reinforced for the generator compartment | □ | □ |  |
| 2.5 Reinforcements to be installed for the mounting of the 4 landing legs – Bulldog 7,000lb side wind droplet landing legs (1 per corner) | □ | □ |  |
| 2.6 Trailer package: 2 – 7000lb Dexter Torflex axles (86”x72” @ 10 degrees down) with side mounting brackets and electric brakes on each axle. 4 – 16” white spoke steel wheels mounted with 4 – ST235/85R16G 14 ply tires Electrical breakaway kit RV style 7 pin trailer plug, lead must extend 18-24” past fully extended hitch | □ | □ |  |
| Paint |
| 3.1 Subframe & running gear to be painted black with self-priming, corrosion resistant paint before installing walls and floor. | □ | □ |  |
| 3.2 Body and entire roof shall be painted white with ESSS 4289 polyurethane paint | □ | □ |  |
| Doors - Steps |
| 4.1 All doors shall be insulated and lined same as interior | □ | □ |  |
| 4.2 Curbside door dimension 42”x80” with 4 stainless steel strap hinges | □ | □ |  |
| 4.3 1 – 24” wide x 24” high thermopane fixed light tint window, hinged cam-lock with inside release kit | □ | □ |  |
| 4.4 Black Bauer BP-12 RV style door handle | □ | □ |  |
| 4.5 Fold out aluminum stairs, 2 – 10” deep diamond-grip channel step rungs, with removable aluminum tubing hand rail. | □ | □ |  |
| 4.6 Steps fold up into trailer for travel (permanently attached), easy one-hand deployment. | □ | □ |  |
| Insulation |
| 5.1 2” urethane spray-foam insulation in walls and ceiling, walls and ceiling ribs furred out | □ | □ |  |
| 5.2 2” urethane spray-foam under floor | □ | □ |  |
| Flooring |
| 6.1 Cross-members – 3” steel I-beam, 16” o.c | □ | □ |  |
| 6.2 ¾” treated plywood sub-floor fully undercoated | □ | □ |  |
| 6.3 LonSeal “Loncoin II Fleck Onyx 150” flooring | □ | □ |  |
| 6.4 Checker plate aluminum covers for insulated steel wheel wells | □ | □ |  |
| Interior Walls & Lining |
| 7.1 Complete interior lined with pre-painted white aluminum | □ | □ |  |
| 7.2 Aluminum bulkhead wall @ 102” from rear wall (this forms the “rear room” area) | □ | □ |  |
| 7.3 Sliding door installed in the bulkhead wall | □ | □ |  |
| Exterior Compartments |
| 8.1 All compartments to be constructed from 1/8” ga aluminum, with extruded aluminum doors. Hinges shall be stainless steel. | □ | □ |  |
| 8.2 Compartments shall be equipped with hinged camlocks for security | □ | □ |  |
| 8.3 Compartment interiors be painted with Zolatone | □ | □ |  |
| 8.4 Inside trailer – compartments to be insulated & lined same as trailer interior | □ | □ |  |
| 8.5 1 - Compartment – roadside approximately 5’ from rear, (sized for 2 - 30lb propane cylinders) 36”wide x 36” high x 18” deep, with double side hinged doors, with one Nailer louver per door | □ | □ |  |
| 8.6 1 - Curbside compartment, approximately 5’ from rear (for storage of 3 - 30lb propane cylinders) 36”wide x 36” high x 20” deep, with double side hinged doors with 1 Nailer louver per door. | □ | □ |  |
| 8.7 1 - Compartment, at front, approximate dimensions 36” wide x ? high x ~20” deep (height TBD by height of bench, double side-hinged doors with 1 Nailor louver in each door. The compartment shall have a heavy duty slide out tray for batteries. Auxiliary battery and 12 volt fuse panel & accessory storage | □ | □ |  |
| 8.8 Draw bar A frame-mounted generator/propane compartment with divider for 2 - 30lb propane tanks. Compartment - 60”wide X 32”high x 28”deep. There shall be double doors for the genset with regular camlock, and single door for propane with hinged camlock – with stainless steel hinges. 1 – Nailor louver per door. | □ | □ |  |
| Interior Layout |
| 9.1 Front Room Benches: "U"-shaped Bench around front section; Black Vinyl covered with lift-up top and back rest, base is formed aluminum "bin" style (seat storage), built in (3) sections (front/Road-Side/Curb-Side) "L"-shaped Bench along Road-Side and divider wall; black vinyl covered with lift-up top and back rest, base formed of aluminum "bin" style" (seat storage) build in 2 - sections (along RS & divider walls), Bench along curb-side wall (between door & divider wall); black vinyl covered top and back rest, base made of support legs - "open" storage under | □ | □ |  |
| 9.2 Front RoomTables: 2 - Pewter Brush Laminate over 3/4" plywood base; aluminum angle nosing with beveled edge, 2 - non-adjustable tubular legs, one table for the "U"-shape bench area, one table for the "L"-shape bench area | □ | □ |  |
| 9.3 Rear Room Lockers: 8 - Aluminum Mesh Lockers - 72"H x 16"D x 18"W; no doors on lockers, fixed shelf @ 16" from floor, fixed shelf @ 12" from top, (3) Double J-Hooks (B#3009122) - in upper area, one on left-side / one on right-side / one @ rear, locker top to have 1" retention lip - serves as shelf | □ | □ |  |
| 9.4 Rear Room Cabinets: Aluminum Storage Cabinet - 72"H x ~30"W x 24"D; double 48” high doors in upper area, doors with formed J-handle & compression latches, 2 "adjustable" shelves in upper area, 2 - 12"H HD Drawers in lower 24" area, with 500lb slides, formed J-handle & compression latches - Storage Cabinet located along divider wall Microwave Shelf - above Curb-Side exterior shelf, install Microwave (see Appliances) Double door Cabinet above "microwave shelf", doors with formed J-handles & compression latches, fixed shelf @ center height | □ | □ |  |
| 9.5 Rear Room Gear Rack: HD Aluminum Rain Gear Rack along rear wall; Full-length "mesh" shelf @ top, 6 - HD hooks for rain gear, (6) "boot racks" - aluminum tubes on angle | □ | □ |  |
| 10. Windows |
| 10.1 All windows to be light tint, 2 - 24"W x 24"H fixed Thermopane window in door (see Access Door section) 1 - 36"W x 36"H slider Thermopane window @ Road-Side; mount above "L"-Bench 1 - 36"W x 36"H slider Thermopane window @ Curb-Side; mount above CS wall Bench | □ | □ |  |
| 10.2 Windows Vandal Protection 2 - Hinged Aluminum Protective Covers for wall Windows; inside pull chain with an upper & lower striker 1 - Removable/Padlockable Protective Cover for Door window | □ | □ |  |
| 11. Generator |
| 11.1 Cummins Onan 6.5kW LP Vapor 120V/240V Genset; 6.5HGJAE-2145 single-phase 2-pole generator, installed (fixed-mounted) in A-Frame front compartment, comes with exhausting through floor as required, plumbed to propane tanks and wired to 12V and 110V panels. Remote Start/Stop Switch with Hour meter installed in Front Room | □ | □ |  |
| 12. Climate Control |
| 12.1 2 - 240V 1000W Stelpro Wall Fan Heaters in Front Room | □ | □ |  |
| 12.2 2 - 240V 1000W Stelpro Wall Fan Heaters in Rear Room, 2 - Wall mount thermostats - one per room | □ | □ |  |
| 12.3 4 - MaxxFan Deluxe Roof Vents (model #7000K); comes with 4 - LCD Wall Controllers (model #00-03000K), 2 - in Front Room & 2 - in Rear Room | □ | □ |  |
| 12.4 1 - Coleman Roughneck HD 15,000 BTU Air Conditioner; roof mount in Front Room area with remote wall mount thermostat | □ | □ |  |
| 13. 12 Volt Electrical Items |
| 13.1 1 - SAMLEX Battery Charger SEC-1250 - 3-stage 12VDC, 50A, install in right side front compartment | □ | □ |  |
| 13.2 2 - 8D Deep Cycle Batteries (EV8DA-A) on slide tray in compartment | □ | □ |  |
| 13.3 1 - DC Panel & Fuses - located close to 12V source | □ | □ |  |
| 13.4 1 - SAMLEX Battery Guard | □ | □ |  |
| 13.5 1 Freedom SW AGS (Auto Gen Start) with network cable, auto recharge batteries when "low" | □ | □ |  |
| 13.6 1 - AM/FM Radio with Bluetooth & 4 ceiling Speakers - radio unit + speakers in front room | □ | □ |  |
| 14. Propane System |
| 14.1 Propane system shall be provided for generator, fridge and heater | □ | □ |  |
| 14.2 2 - 30lb cylinders installed in vented A-frame compartment; comes with regulator & plumbing to Generator, 2 - bottle propane storage rack | □ | □ |  |
| 14.2 2 - 30lb cylinders installed in right side compartment, comes with regulator & plumbing to Heater, 2-bottle propane storage rack | □ | □ |  |
| 14.3 3 - 30lb cylinders installed in vented rear passenger side compartment, these are "spare" bottles - stored in compartment, in propane bottle storage racks | □ | □ |  |
| 14.4 1 - 35,000 BTU ATWOOD RV Furnace (propane/12V)(8535 / 1053-9); comes with 85-series Door (Polar White #9210-485) wall mount thermostat, mount on road-side under bench ducted to both rooms | □ | □ |  |
| 15. Appliances |
| 15.1 1 - Stainless Steel Microwave - 1000W | □ | □ |  |
| 15.2 1 - Fridge: Domestic RM2554LB / 5 cu.ft. (Propane/120V); installed in rear room | □ | □ |  |
| 16. Other |
| 16.1 Trailer certified to meet CMVSS regulations including all Provincial and Federal Regulations | □ | □ |  |
| 16.2 Trailer supplied with Motor Vehicle Inspection Certificate | □ | □ |  |
| 16.3 Full AutoCAD drawings to be provided to CoS after awarding of tender for CoS approval | □ | □ |  |
| 16.4 Wiring Diagram for 12V & 120V | □ | □ |  |
| 16.5 3 - sets of keys to be included | □ | □ |  |

2.	In addition to the warranties provided in the Agreement, this Quotation includes the following warranties:

3.	I/We have reviewed the RFQ Attachment 1, Schedule A – Specifications of Goods and if requested by the City, I/we would be prepared to meet those requirements, amended by the following departures and additions (list, if any):

Requested Departure(s) / Alternative(s) / Addition(s)

The City is not obligated to accept any alternatives. The City will determine what constitutes acceptable deviations and overall best value.

4.	If this Quotation is accepted by the City, a contract will be created as described in:

(a)	the Agreement;

(b)	the RFQ; and

(c)	other terms, if any, that are agreed to by the parties in writing.

5.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

6.	I/We have reviewed the RFQ Attachment 1 – Draft Agreement. If requested by the City, I/we would be prepared to enter into that Agreement, amended by the following departures (list, if any):

Section			Requested Departure(s) / Alternative(s)

7.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |