|  | SCHEDULE B – FORM OF QUOTATION |
| --- | --- |

RFQ Title:	SUPPLY AND DELIVERY OF THREE (3) OR MORE THREE

QUARTER TON DUAL FUEL (CNG & GASOLINE) TRUCKS IN VARIOUS 	CONFIGURATIONS

RFQ No:	1220-040-2017-045

CONTRACTOR

Legal Name:

Address:

Phone:

Fax:

Email:

CITY OF SURREY

TO:

City Representative:	Richard D. Oppelt

Purchasing Manager

Address:		Surrey City Hall

Finance & Technology Department – Purchasing Section

Reception Counter, 5th Floor West

13450 – 104th Avenue, Surrey, B.C., V3T 1V8

Telephone:		604-590-7274

Email:			purchasing@surrey.ca

QUOTATION UNIT PRICING TABLES

The Contractor offers to supply to the City of Surrey the Goods for the unit prices plus applicable

fees as follows (GST & PST extra):

QUOTATION 1 – THREE QUARTER TON REGULAR CAB

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications should be included in the following delivered prices.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | THREE QUARTER TON REGULAR CAB |
| VEHICLE QUANTITY | 1 | 2 | 3 | 3+ (PER VEHICLE) |
| UNIT PRICE (Per Vehicle) | $_______ | $_______ | $_______ | $_______ |
| ENVIRONMENTAL LEVY [BATTERY] | $_______ | $_______ | $_______ | $_______ |
| TIRE STEWARDSHIP B.C. (TSBC) | $_______ | $_______ | $_______ | $_______ |
| OTHER: |  |  |  |  |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Contractor shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 8’ box or provide dimensions | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Vent visors to be fitted to both front door windows |  |  |  |
| Engine |
| 2.1 Engine shall be prepared to run on CNG and gasoline | □ | □ |  |
| 2.2 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.3 Cooling system to -30F | □ | □ |  |
| 2.4 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| 2.5 State engine capacity, configuration, and hp | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 Fuel tanks must be mounted to the vehicle in a manner to maximize box space. The tanks shall be mounted above the floor of the deck, with approximately 7” clearance | □ | □ |  |
| 4.5 CNG tank shall have an aluminum checker plate cover which protects the tank. The aluminum checker plate shall be a minimum of 3mm in thickness. The cover shall be securely attached to the box. The bottom of the tank shall be protected with 3mm aluminum plate | □ | □ |  |
| 4.6 The mounting of the tanks shall be certified by a qualified engineer. | □ | □ |  |
| 4.7 A hinged access flap shall be provided in the top of the cover for access to the tank shut off valve |  |  |  |
| 4.8 The CNG filling port shall be located as close as possible to the gasoline filler | □ | □ |  |
| 4.9 Please install equipment as part of the installation that will allow for de-fueling of the CNG system including tank. | □ | □ |  |
| Wheels, Tires |
| 5.1 Michelin winter tires (snow flake) | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.3 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.4 Air conditioning | □ | □ |  |
| 6.5 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 3 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package 1 – Complete hidden trailer hitch package, c/w receiver, hitch to match the maximum towing capability of the vehicle. Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 Spray-in bed liner, under rail, including tailgate | □ | □ |  |
| 7.4 State GVW in lbs | □ | □ |  |
| 7.5 State max towing capacity in lbs | □ | □ |  |
| 7.6 Aluminum cab guard – mesh type (Brand - DeeZee) | □ | □ |  |
| 7.7 Beacon light – LED amber Whelen (R2LPPA), to be mounted on cab guard to the left side of the vehicle. Light to be wired separately of the ignition switch. Switch to be illuminated when on. | □ | □ |  |
| 7.8 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.9 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.10 Splash guards front and rear | □ | □ |  |
| 7.11 Running boards shall be supplied and fitted | □ | □ |  |
| 7.12 The vehicle shall be rust proofed with a product that provides long term protection, and does not require continued reapplication of the product. Proponent to provide details of product offered and warranty. | □ | □ |  |
| 7.13 The proponent shall deliver the vehicles, registered, insured, and plated as per the City’s insurance requirements through the City’s insurance broker. | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |

QUOTATION 2 – THREE QUARTER TON REGULAR CAB 4X4

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications shall be included in the following delivered prices. GST & PST extra.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | THREE QUARTER TON REGULAR CAB 4X4 |
| VEHICLE QUANTITY | 1 | 2 | 3 | 3+ (PER VEHICLE) |
| UNIT PRICE (Per Vehicle) | $_______ | $_______ | $_______ | $_______ |
| ENVIRONMENTAL LEVY [BATTERY] | $_______ | $_______ | $_______ | $_______ |
| TIRE STEWARDSHIP B.C. (TSBC) | $_______ | $_______ | $_______ | $_______ |
| OTHER: |  |  |  |  |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 8’ box or provide dimensions | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Vent visors to be fitted to both front door windows |  |  |  |
| Engine |
| 2.1 Engine shall be prepared to run on CNG and gasoline | □ | □ |  |
| 2.2 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.3 Cooling system to -30F | □ | □ |  |
| 2.4 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| 2.5 State engine capacity, configuration, and hp | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| 3.4 Front axle shall have freewheeling hubs | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 Fuel tanks must be mounted to the vehicle in a manner to maximize box space. The tanks shall be mounted above the floor of the deck, with approximately 7” clearance | □ | □ |  |
| 4.5 CNG tank shall have an aluminum checker plate cover which protects the tank. The aluminum checker plate shall be a minimum of 3mm in thickness. The cover shall be securely attached to the box. The bottom of the tank shall be protected with 3mm aluminum plate | □ | □ |  |
| 4.6 The mounting of the tanks shall be certified by a qualified engineer. | □ | □ |  |
| 4.7 A hinged access flap shall be provided in the top of the cover for access to the tank shut off valve | □ | □ |  |
| 4.8 The CNG filling port shall be located as close as possible to the gasoline filler | □ | □ |  |
| 4.9 Please install equipment as part of the installation that will allow for de-fueling of the CNG system including tank. | □ | □ |  |
| Wheels, Tires |
| 5.1 Michelin winter tires (snow flake) | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.3 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.4 Air conditioning | □ | □ |  |
| 6.5 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 3 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package 1 – Complete hidden trailer hitch package, c/w receiver, hitch to match the maximum towing capability of the vehicle. Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 Spray-in bed liner, under rail, including tailgate | □ | □ |  |
| 7.4 State GVW in lbs | □ | □ |  |
| 7.5 State max towing capacity in lbs | □ | □ |  |
| 7.6 Aluminum cab guard – mesh type (Brand - DeeZee) | □ | □ |  |
| 7.7 Beacon light – LED amber Whelen (R2LPPA), to be mounted on cab guard to the left side of the vehicle. Light to be wired separately of the ignition switch. Switch to be illuminated when on. | □ | □ |  |
| 7.8 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.9 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.10 Splash guards front and rear | □ | □ |  |
| 7.11 Running boards shall be supplied and fitted | □ | □ |  |
| 7.12 The vehicle shall be rust proofed with a product that provides long term protection, and does not require continued reapplication of the product. Proponent to provide details of product offered and warranty. | □ | □ |  |
| 7.13 The proponent shall deliver the vehicles, registered, insured, and plated as per the City’s insurance requirements through the City’s insurance broker. | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |

3.  QUOTATION 3 – THREE QUARTER TON EXTENDED CAB 4X2

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications shall be included in the following delivered prices. GST & PST extra

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | THREE QUARTER TON EXTENDED CAB 4x2 |
| VEHICLE QUANTITY | 1 | 2 | 3 | 3+ (PER VEHICLE) |
| UNIT PRICE (Per Vehicle) | $_______ | $_______ | $_______ | $_______ |
| ENVIRONMENTAL LEVY [BATTERY] | $_______ | $_______ | $_______ | $_______ |
| TIRE STEWARDSHIP B.C. (TSBC) | $_______ | $_______ | $_______ | $_______ |
| OTHER: |  |  |  |  |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 8’ box or provide dimensions | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Vent visors to be fitted to both front door windows | □ | □ |  |
| Engine |
| 2.1 Engine shall be prepared to run on CNG and gasoline | □ | □ |  |
| 2.2 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.3 Cooling system to -30F | □ | □ |  |
| 2.4 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| 2.5 State engine capacity, configuration, and hp | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 Fuel tanks must be mounted to the vehicle in a manner to maximize box space. The tanks shall be mounted above the floor of the deck, with approximately 7” clearance | □ | □ |  |
| 4.5 CNG tank shall have an aluminum checker plate cover which protects the tank. The aluminum checker plate shall be a minimum of 3mm in thickness. The cover shall be securely attached to the box. The bottom of the tank shall be protected with 3mm aluminum plate | □ | □ |  |
| 4.6 The mounting of the tanks shall be certified by a qualified engineer. | □ | □ |  |
| 4.7 A hinged access flap shall be provided in the top of the cover for access to the tank shut off valve | □ | □ |  |
| 4.8 The CNG filling port shall be located as close as possible to the gasoline filler | □ | □ |  |
| 4.9 Please install equipment as part of the installation that will allow for de-fueling of the CNG system including tank. | □ | □ |  |
| Wheels, Tires |
| 5.1 Michelin winter tires (snow flake) | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 Rear seats shall be bench type with the ability for the seat to fold up | □ | □ |  |
| 6.3 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.4 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.5 Air conditioning | □ | □ |  |
| 6.6 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 3 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package 1 – Complete hidden trailer hitch package, c/w receiver, hitch to match the maximum towing capability of the vehicle. Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 Spray-in bed liner, under rail, including tailgate | □ | □ |  |
| 7.4 State GVW in lbs | □ | □ |  |
| 7.5 State max towing capacity in lbs | □ | □ |  |
| 7.6 Aluminum cab guard – mesh type (Brand - DeeZee) | □ | □ |  |
| 7.7 Beacon light – LED amber Whelen (R2LPPA), to be mounted on cab guard to the left side of the vehicle. Light to be wired separately of the ignition switch. Switch to be illuminated when on. | □ | □ |  |
| 7.8 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.9 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.10 Splash guards front and rear | □ | □ |  |
| 7.11 Running boards shall be supplied and fitted | □ | □ |  |
| 7.12 The vehicle shall be rust proofed with a product that provides long term protection, and does not require continued reapplication of the product. Proponent to provide details of product offered and warranty. | □ | □ |  |
| 7.13 The proponent shall deliver the vehicles, registered, insured, and plated as per the City’s insurance requirements through the City’s insurance broker. | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |

4.  QUOTATION 4 – THREE QUARTER TON EXTENDED CAB 4X4

Year, Make & Model:  __________________________________________________________

All costs to meet the preferred specifications shall be included in the following delivered prices. GST & PST Extra.

| F.O.B. | Payment Terms: | Ship Via: |
| --- | --- | --- |
| Destination Freight Prepaid | A cash discount of ____% will be allowed if invoices are paid within ___ days, or the ___ day of the month following, or net 30 days, on a best effort basis. |  |
| ITEM | THREE QUARTER TON EXTENDED CAB 4X4 |
| VEHICLE QUANTITY | 1 | 2 | 3 | 3+ (PER VEHICLE) |
| UNIT PRICE (Per Vehicle) | $_______ | $_______ | $_______ | $_______ |
| ENVIRONMENTAL LEVY [BATTERY] | $_______ | $_______ | $_______ | $_______ |
| TIRE STEWARDSHIP B.C. (TSBC) | $_______ | $_______ | $_______ | $_______ |
| OTHER: |  |  |  |  |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| ____________________________ | $_______ | $_______ | $_______ | $_______ |
| CURRENCY: CANADIAN |  |  |  |  |

The completed unit shall be delivered within _______ days after receipt of purchase order.

Manufacturer’s Warranty:  State Warranty

Body Warranty:  State Warranty________________________________________________________

Warranty repairs shall be performed at

Please complete if applicable:	British Columbia Certified (

Note: Contractors are directed to list complete manufacturers’ details of model proposed in the right-side column under manufacturers’ specifications

| Preferred Specifications | √ (Yes) | √ (No) | Manufacturers’ Specifications of Equipment Offered. Bidder shall complete all spaces in this column. |
| --- | --- | --- | --- |
| Exterior |
| 1.1 Colour - White | □ | □ |  |
| 1.2 8’ box or provide dimensions | □ | □ |  |
| 1.3 Heated mirrors | □ | □ |  |
| 1.4 Vent visors to be fitted to both front door windows |  |  |  |
| Engine |
| 2.1 Engine shall be prepared to run on CNG and gasoline | □ | □ |  |
| 2.2 Full manufactures warranty with CNG conversion must be provided | □ | □ |  |
| 2.3 Cooling system to -30F | □ | □ |  |
| 2.4 CNG system to be integrated into manufacturer’s engine management system. Only factory approved conversions will be acceptable | □ | □ |  |
| 2.5 State engine capacity, configuration, and hp | □ | □ |  |
| Transmission, Brakes |
| 3.1 Automatic transmission, state number of speeds | □ | □ |  |
| 3.2 Power assisted ABS brakes | □ | □ |  |
| 3.3 Limited slip differential | □ | □ |  |
| 3.4 Front axle shall have freewheeling hubs | □ | □ |  |
| Fuel Tanks |
| 4.1 The manufacturers gasoline fuel tank shall remain | □ | □ |  |
| 4.2 CNG tank(s) shall be a size of at least 24.5 GGE/93GLE to give sufficient operating range under normal operating conditions and shall be made of composite material – steel tanks are unacceptable | □ | □ |  |
| 4.3 Fuel gauge for each fuel type shall be provided in easy view for the driver | □ | □ |  |
| 4.4 Fuel tanks must be mounted to the vehicle in a manner to maximize box space. The tanks shall be mounted above the floor of the deck, with approximately 7” clearance | □ | □ |  |
| 4.5 CNG tank shall have an aluminum checker plate cover which protects the tank. The aluminum checker plate shall be a minimum of 3mm in thickness. The cover shall be securely attached to the box. The bottom of the tank shall be protected with 3mm aluminum plate | □ | □ |  |
| 4.6 The mounting of the tanks shall be certified by a qualified engineer. | □ | □ |  |
| 4.7 A hinged access flap shall be provided in the top of the cover for access to the tank shut off valve |  |  |  |
| 4.8 The CNG filling port shall be located as close as possible to the gasoline filler | □ | □ |  |
| 4.9 Please install equipment as part of the installation that will allow for de-fueling of the CNG system including tank. | □ | □ |  |
| Wheels, Tires |
| 5.1 Michelin winter tires (snow flake) | □ | □ |  |
| 5.2 Full size spare tire | □ | □ |  |
| Interior |
| 6.1 Seats 40/20/40 split front seat, vinyl covered | □ | □ |  |
| 6.2 Rear seats shall be bench type with the ability for the seat to fold up | □ | □ |  |
| 6.3 2 – 12 volt power outlets shall be provided | □ | □ |  |
| 6.4 Rubber Floor Mats shall be provided for all seating areas | □ | □ |  |
| 6.5 Air conditioning | □ | □ |  |
| 6.6 AM/FM radio with Bluetooth | □ | □ |  |
| Miscellaneous |
| 7.1 Keyless entry with 3 sets of keys | □ | □ |  |
| 7.2 Trailer Tow Package 1 – Complete hidden trailer hitch package, c/w receiver, hitch to match the maximum towing capability of the vehicle. Wiring to match 6 pin 1235 BX Cole Hersey t/plug and brake controller | □ | □ |  |
| 7.3 Spray-in bed liner, under rail, including tailgate | □ | □ |  |
| 7.4 State GVW in lbs | □ | □ |  |
| 7.5 State max towing capacity in lbs | □ | □ |  |
| 7.6 Aluminum cab guard – mesh type (Brand - DeeZee) | □ | □ |  |
| 7.7 Beacon light – LED amber Whelen (R2LPPA), to be mounted on cab guard to the left side of the vehicle. Light to be wired separately of the ignition switch. Switch to be illuminated when on. | □ | □ |  |
| 7.8 Back up alarm - Grote part # 73040 97 dBA | □ | □ |  |
| 7.9 Fire extinguisher 2.5lb dry powder ABC type | □ | □ |  |
| 7.10 Splash guards front and rear | □ | □ |  |
| 7.11 Running boards shall be supplied and fitted | □ | □ |  |
| 7.12 The vehicle shall be rust proofed with a product that provides long term protection, and does not require continued reapplication of the product. Proponent to provide details of product offered and warranty. | □ | □ |  |
| 7.13 The proponent shall deliver the vehicles, registered, insured, and plated as per the City’s insurance requirements through the City’s insurance broker. | □ | □ |  |
| CNG |
| 8.1 The vehicles shall default to run on CNG, and shall only operate on gasoline when the CNG tanks are empty. Vehicles may start on gasoline but must automatically switch to CNG once they reach operating temperature. (Please provide details) | □ | □ |  |
| Warranty |
| 9.1 Provide details of manufacturer’s warranty | □ | □ |  |
| 9.2 Operators Manuals / Service Manuals 1 – Service manual or CD c/w software | □ | □ |  |

2.		If this offer is accepted by the City, such offer and acceptance will create a contract as described in:

(a)	the RFQ;

(b)	the specifications set out above and in Schedule A of the RFQ;

(c)	the General Terms and Conditions;

(d)	this Quotation; and

(e)	other terms, if any, that are agreed to by the parties in writing.

3.		Capitalized terms used and not defined in this Quotation will have the meanings given to them in the RFQ.  Except as specifically modified by this Quotation, all terms, conditions, representations, warranties and covenants as set out in the RFQ will remain in full force and effect.

4.	The Contractor to indicate on each line provided in Schedule B if they comply with the Quote items as specified or are taking exception to the Quote items specified.

If additional space is required to fully explain Quote exception(s), attach additional page(s) to the Quotation and indicate the section number and subsection that has the exception and provide explanation.

If more than one (1) make or model is to be offered, copy the specification sheets to submit separate Quotation sheets for each item to be evaluated.

5.	I/We the undersigned duly authorized representatives of the Contractor, having received and carefully reviewed the RFQ including without limitation the Specifications and the General Terms and Conditions, submit this Quotation in response to the RFQ.

-END OF PAGE-

This Quotation is offered by the Contractor this _______ day of _______________, 201_.

CONTRACTOR

I/We have the authority to bind the Contractor

| ________________________________________ (Legal Name of Contractor) _________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) | ________________________________________ (Signature of Authorized Signatory) ________________________________________ (Print Name and Position of Authorized Signatory) |
| --- | --- |

This Quotation is accepted by the City this _______ day of _______________, 201_.

CITY OF SURREY

| ________________________________________ (Signature of Authorized Signatory) _________________________________________ (Print Name and Position of Authorized Signatory) _________________________________________ (Signature of Authorized Signatory) | ________________________________________ (Signature of Purchasing Representative ________________________________________ (Print Name of Purchasing Representative) |
| --- | --- |

| _________________________________________ (Print Name and Position of Authorized Signatory) |  |
| --- | --- |